## Slide 1: BCT 2408 Computer Architecture
Jeff Gicharu – SCT212-0053/2021
Fundamentals of Computer Design

## Slide 2: Introduction to Computer Architecture
Rapid Progress in Computer Technology
  Computer technology has made incredible progress in the roughly 65 years since the first general-purpose electronic computer was created.
  Example: Today, less than $500 will purchase a personal computer that has more performance, more main memory, and more disk storage than a computer bought in 1985 for 1 million dollars.
  This progress is driven by both technological advancements and innovative computer design.
  Microprocessors and Performance Improvement
  The emergence of microprocessors in the late 1970s led to significant performance gains.
  The ability of the microprocessor to ride the improvements in integrated circuit technology led to a higher rate of improvement which was roughly 35% growth per year in performance.
  This growth, combined with cost advantages, led to the dominance of microprocessors in the computer industry.

## Slide 3: Introduction to Computer Architecture
  Impact of New Architectures
  The development of RISC (Reduced Instruction Set Computer) architectures in the early 1980s raised the performance bar.
  The RISC-based machines focused the attention of designers on two critical performance techniques, the exploitation of instruction-level parallelism (initially through pipelining and later through multiple instruction issue) and the use of caches (initially in simple forms and later using more sophisticated organizations and optimizations).
  This innovation forced other architectures to adapt or become obsolete.

## Slide 4: Evolution of Computer Architecture
Historical Performance Growth
  From the mid-1980s to 2002, processor performance grew at an unprecedented rate of over 50% per year.
  This growth was driven by architectural and organizational enhancements, such as pipelining and sophisticated cache designs.
  By 2002, high-performance microprocessors were seven times faster than what could have been achieved with technology alone.
  Changing Landscape of Computing
  The dramatic improvement in performance led to new classes of computers, such as personal computers and workstations.
  Minicomputers were replaced by microprocessor-based servers, and mainframes were replaced by multiprocessors.
  Even high-end supercomputers began to be built using collections of microprocessors.

## Slide 5: Evolution of Computer Architecture
  Modern Challenges
  Since 2002, performance improvement has slowed to about 20% per year due to power limitations, memory latency, and reduced ILP.
  The industry shifted focus from ILP to thread-level parallelism (TLP) and data-level parallelism (DLP) to achieve further performance gains.

## Slide 6: Classes of Computers – Desktop Computing
Desktop Computing Overview
  Desktop computing is the largest market in dollar terms, ranging from low-end netbooks to high-end workstations.
  Key characteristics include price-performance optimization, graphics performance, and responsiveness.
  The market is driven by consumer needs for balanced performance across various tasks, including interactive applications.
  Market Drivers
  The newest, highest-performance microprocessors often debut in desktop systems due to the demand for high performance at a reasonable cost.
  Applications are well-characterized, though the increasing use of web-centric applications poses new challenges in performance evaluation.
  Example: A high-end workstation might be used for professional graphics design, requiring powerful processors and graphics cards.

## Slide 7: Classes of Computers – Servers
Server Computing Overview
  Servers provide large-scale, reliable file and computing services, replacing traditional mainframes.
  Key characteristics include dependability, scalability, and efficient throughput.
  Servers must operate 24/7, making reliability and availability critical.
  Market Drivers
  Dependability is crucial, with significant financial losses associated with downtime.
  Scalability is essential as server demands grow, requiring the ability to increase computing capacity, memory, storage, and I/O bandwidth.
  Example: Google's servers handle billions of search queries daily, requiring high availability and scalability.

## Slide 8: Classes of Computers – Embedded Systems
Embedded Systems Overview
  Embedded computers are found in everyday devices, from microwaves and printers to cars and cell phones.
  Key characteristics include low cost, low power consumption, and application-specific performance.
  Performance requirements are often real-time, with strict constraints on execution time.
  Market Drivers
  Price is a critical factor, with a focus on meeting performance needs at the lowest possible cost.
  Energy efficiency is driven by battery life and heat dissipation concerns.
  Example: A digital set-top box must process video frames in real-time, requiring efficient use of limited resources.

## Slide 9: Embedded Systems – Characteristics and Applications
Characteristics of Embedded Systems
  Wide Range of Processing Power: From simple 8-bit processors to high-end 64-bit processors capable of executing billions of instructions per second.
  Cost Sensitivity: Design often focuses on meeting performance needs at the minimum cost.
  Real-Time Performance: Many applications require real-time execution, with strict constraints on maximum execution time.
  Power and Memory Optimization: Minimizing power consumption and memory usage are critical, especially in battery-powered devices.
  Applications of Embedded Systems
  Consumer Electronics: Microwaves, washing machines, printers, and digital set-top boxes.
  Mobile Devices: Smartphones and tablets with multimedia capabilities.
  Automotive: Modern cars contain multiple embedded systems for various functions, from engine control to infotainment.
  Networking: Routers, switches, and other network infrastructure devices.

## Slide 10: Embedded Systems – Design Considerations
Design Challenges
  Low Power Consumption: Essential for battery-operated devices and to reduce heat generation.
  Minimized Memory Usage: Optimizing code size and data structures to fit within limited memory resources.
  Real-Time Constraints: Ensuring that critical tasks meet their deadlines, even under varying load conditions.
  Reliability: Ensuring robust operation in potentially harsh environments.
  Future Trends
  Increased Integration: More functions integrated into a single chip to reduce cost and improve performance.
  Energy Efficiency: Continued focus on reducing power consumption to extend battery life and reduce environmental impact.
  Security: Enhanced security measures to protect against vulnerabilities in connected devices.

## Slide 11: Defining Computer Architecture
Role of the Computer Architect
  The computer architect's task is to design a computer that maximizes performance while staying within constraints of cost, power, and availability.
  This involves understanding a wide range of technologies, from compilers and operating systems to logic design and packaging.
  Components of Computer Design
  Instruction Set Architecture (ISA): The boundary between software and hardware, defining the instructions visible to the programmer.
  Organization: The high-level design aspects, including memory systems, interconnects, and processor design.
  Hardware: The detailed logic design and packaging technology.

## Slide 12: Instruction Set Architecture (ISA)
ISA Dimensions
  Class of ISA: General-purpose register architectures, with operands as registers or memory locations.
  Memory Addressing: Byte addressing, with alignment requirements for some architectures.
  Addressing Modes: Various ways to specify memory addresses, including register, immediate, and displacement modes.
  Types and Sizes of Operands: Support for multiple operand sizes, including integers and floating-point numbers.
  Operations: Categories include data transfer, arithmetic/logical operations, control flow, and floating-point operations.
  Encoding
  Fixed-length (e.g., MIPS) or variable-length (e.g., x86) instructions, affecting instruction decoding complexity.

## Slide 13: Organization and Hardware in Computer Design
Organization
  Memory System: Design of main memory, caches, and memory hierarchy.
  Processor Design: Pipeline design, cache organization, and instruction scheduling.
  Interconnects: Design of buses and networks for communication between components.
  Hardware
  Detailed Logic Design: Implementation of specific logic circuits and control units.
  Packaging Technology: Physical packaging and cooling solutions to manage power dissipation.
  Performance Optimization: Techniques to improve performance, such as speculative execution and out-of-order processing.

## Slide 14: Challenges Beyond ISA Design
Beyond ISA: The Bigger Picture
  While ISA design is crucial, modern computer architecture involves much more.
  Microarchitecture: Detailed design of the CPU, including pipeline stages, cache design, and execution units.
  System Organization: High-level design aspects such as memory hierarchy, interconnects, and I/O systems.
  Hardware Implementation: Detailed logic design, packaging, power management, and cooling solutions.
  Modern Architectural Challenges
  Power Management: Balancing performance with power consumption, especially in mobile and embedded devices.
  Thermal Design: Ensuring efficient heat dissipation to prevent overheating and maintain performance.
  Scalability: Designing systems that can scale up in terms of performance, memory, and storage.
  Reliability: Ensuring system dependability, especially in critical applications like servers and embedded systems.

## Slide 15: Functional Requirements in Computer Architecture
Key Functional Requirements
  Application Area: Tailoring the architecture to specific use cases like desktops, servers, or embedded systems.
  Software Compatibility: Ensuring compatibility with existing software ecosystems through instruction set design.
  Operating System Support: Providing necessary features to support modern operating systems.
  Address Space: Defining the size of addressable memory space.
  Memory Management: Implementing efficient memory management techniques like paging and segmentation.
  Protection: Ensuring security and isolation between different processes and users.
  Standards and Interfaces
  Adhering to industry standards for floating-point arithmetic, I/O interfaces, and networking.
  Supporting various programming languages and development frameworks.

## Slide 16: Trends in Technology
Rapid Technological Advancements
  Computer architecture must adapt to rapid changes in technology to remain relevant.
  Key technologies include integrated circuit logic, DRAM, Flash memory, magnetic disks, and networking.
  Moore’s Law and its Impact
  Transistor Density: Transistor density increases by about 35% per year, doubling every 18 to 24 months.
  Performance Improvements: Device speed scales more slowly, but improvements in density lead to significant performance gains.
  Cost Reduction: Technological advancements reduce the cost of components, making high-performance computing more accessible.

## Slide 17: Trends in Memory and Storage
DRAM Trends
  Capacity Growth: DRAM capacity has been increasing by about 25% to 40% per year, doubling every two to three years.
  Performance: Improvements in bandwidth and latency, though latency improvements are slower compared to bandwidth.
  Cost: DRAM remains a cost-effective solution for main memory, with prices dropping over time.
  Flash Memory
  Rapid Growth: Flash memory capacity is increasing rapidly, making it a popular choice for mobile and embedded devices.
  Performance: Significant improvements in read/write speeds and overall performance.
  Cost: Flash memory is becoming increasingly cost-effective, challenging traditional storage solutions.

## Slide 18: Trends in Networking and Future Directions
Networking Trends
  Bandwidth Improvements: Network bandwidth has seen significant increases, from 10 Mbps to 100 Gbps.
  Latency Reduction: Latency improvements, though not as dramatic as bandwidth, are still significant.
  Technological Advances: Adoption of new standards and technologies like Ethernet, InfiniBand, and wireless networking.
  Future Directions
  Energy Efficiency: Increasing focus on energy-efficient designs to reduce power consumption.
  Scalability: Designing systems that can scale efficiently to meet growing demands.
  Integration: Continued integration of multiple processors and functionalities into single chips.
  Reliability: Ensuring system reliability and fault tolerance in the face of increasing complexity.

## Slide 19: Performance Trends in Technology
Performance Metrics
  Bandwidth vs. Latency: Bandwidth measures the total amount of work done in a given time, while latency measures the time between the start and completion of an event.
  Improvement Rates: Bandwidth improvements have outpaced latency improvements significantly across microprocessors, memory, networks, and disks.
  Rule of Thumb: Bandwidth grows by at least the square of the improvement in latency.
  Impact on Design
  Microprocessors: Focus on increasing throughput and parallelism.
  Memory: Emphasis on increasing capacity and bandwidth, with moderate latency improvements.
  Disks: Continued growth in storage density, with improvements in both bandwidth and latency.
  Networks: Significant increases in bandwidth, with latency improvements driven by advancements in switch and transmission technologies.

## Slide 20: Scaling of Transistor Performance and Wires
Transistor Performance
  Feature Size Reduction: Transistor density increases quadratically with a linear decrease in feature size.
  Performance Improvement: Transistor performance improves linearly with decreasing feature size.
  Impact: Higher transistor density and performance enable more complex and efficient designs.
  Wire Delay
  Signal Delay: Wire delay scales poorly compared to transistor performance, increasing proportionally to the product of resistance and capacitance.
  Challenges: Wire delay has become a significant design limitation, often more critical than transistor switching delay.
  Technological Enhancements: Introducing materials like copper has provided one-time improvements in wire delay.

## Slide 21: Trends in Power and Energy in Integrated Circuits
Power Consumption
  Dynamic Power: Dominant energy consumption in CMOS chips, proportional to the product of capacitive load, voltage squared, and switching frequency.
  Static Power: Increasingly significant due to leakage current, even when transistors are off.
  Voltage Scaling: Reducing voltage significantly lowers dynamic power and energy consumption.
  Energy Efficiency
  Energy vs. Power: Energy is a better metric for comparing processors, as it ties performance to a specific task and execution time.
  Techniques for Efficiency: Dynamic Voltage-Frequency Scaling (DVFS), power gating, and designing for typical use cases.

## Slide 22: Trends in Cost
Cost Factors
  Manufacturing Costs: Decrease over time due to the learning curve and yield improvements.
  Volume: Higher volumes reduce cost through increased efficiency and purchasing power.
  Commoditization: Standardized components lead to lower costs and increased competition.
  Integrated Circuit Costs
  Wafer Cost: Dominant factor in the cost of producing integrated circuits.
  Die Yield: Number of good dies per wafer, influenced by defect density and process complexity.
  Mask Costs: Significant fixed cost for low-volume production, affecting prototyping and debugging.
  Cost vs Price
  Manufacturing Margins: Narrowing due to commoditization, with R&D and marketing costs impacting final price.
  Operational Costs: Significant for large-scale data centers and warehouse-scale computers, emphasizing energy efficiency.